## Slide 1: Modern Control Systems
Lecture-1
Introduction to Compensation

## Slide 2: Lecture Outline
Introduction to compensation
Compensation via root Locus
Compensator Configurations
Commonly Used Compensators
Effect of Adding Poles and Zeros on Root locus

## Slide 3: Introduction
A feedback control system that provides an optimum performance without any necessary adjustment is rare.
In building a control system, we know that proper modification of the plant dynamics may be a simple way to meet the performance specifications.
This, however, may not be possible in many practical situations because the plant may be fixed and not modifiable.
Then we must adjust parameters other than those in the fixed plant.

## Slide 4: Introduction
In previous lectures, we have discussed root locus method for loop gain adjustment.
We have found that to achieve the desired system response, it is possible to adjust the system parameters but it is often not enough.
Desired Closed Loop Pole

## Slide 5: Introduction
It is then required to reconsider the structure of the system and redesign the system.
The design problems, therefore, become those of improving system performance by insertion of a compensator.
Compensator: A compensator is an additional component or circuit that is inserted into a control system to equalize or compensate for a deficient performance.

## Slide 6: Introduction
Necessities of compensation
A system may be unsatisfactory in：
  Stability.
  Speed of response.
  Steady-state error.
Thus the design of a system is concerned with the alteration of the frequency response or the root locus of the system in order to obtain a suitable system performance.

## Slide 7: Compensation via Root Locus
Performance measures in the time domain:
  Peak time;
  Overshoot;
  Settling time for a step input;
  Steady-state error for test inputs
These performance specifications can be defined in terms of the desirable location of the poles and zeros of the closed-loop.
Root locus method can be used to find a suitable compensator Gc(s) so that the resultant root locus results in the desired closed-loop root configuration.

## Slide 8: Compensation via Root Locus
The design by the root-locus method is based on reshaping the root locus of the system by adding poles and zeros to the system’s open-loop transfer function and forcing the root loci to pass through desired closed-loop poles in the s plane.
The characteristic of the root-locus design is its being based on the assumption that the closed-loop system has a pair of dominant closed-loop poles.
This means that the effects of zeros and additional poles do not affect the response characteristics very much.

## Slide 9: Compensator Configurations
Compensation schemes commonly used for feedback control systems are:
  Series Compensation
  Parallel Compensation

## Slide 10: Compensator Configurations
The choice between series compensation and parallel compensation depends on
  the nature of the signals
  the power levels at various points
  available components
  the designer’s experience
  economic considerations and so on.

## Slide 11: Commonly Used Compensators
Among the many kinds of compensators, widely employed compensators are the
  lead compensators
  lag compensators
  lag–lead compensators

## Slide 12: Commonly Used Compensators
Among the many kinds of compensators, widely employed compensators are the
  lead compensators
    If a sinusoidal input is applied to the input of a network, and the steady-state output (which is also sinusoidal) has a phase lead, then the network is called a lead network.

## Slide 13: Commonly Used Compensators
Among the many kinds of compensators, widely employed compensators are the
  lag compensators
    If the steady-state output has a phase lag, then the network is called a lag network.

## Slide 14: Commonly Used Compensators
Among the many kinds of compensators, widely employed compensators are the
  lag–lead compensators
    In a lag–lead network, both phase lag and phase lead occur in the output but in different frequency regions.
    Phase lag occurs in the low-frequency region and phase lead occurs in the high-frequency region.

## Slide 15: Commonly Used Compensators
We will limit our discussions mostly to lead, lag, and lag–lead compensators realized by
  Electronic devices such as circuits using operational amplifiers
  Electrical Networks (RC networks)
  Mechanical Networks (Spring-Mass-Damper Networks).

## Slide 16: Effect of Addition of Poles on Root Locus
The addition of a pole to the open-loop transfer function has the effect of pulling the root locus to the right, tending to lower the system’s relative stability and to slow down the settling of the response.

## Slide 17
Effect of Addition of poles
Add a Pole at -1

## Slide 18
Effect of Addition of poles

## Slide 19: Effect of Addition of Zeros on Root Locus
The addition of a pole to the open-loop transfer function has the effect of pulling the root locus to the right, tending to lower the system’s relative stability and to slow down the settling of the response.

## Slide 20
Effect of Addition of zeros
Add a zero at -3

## Slide 21
Effect of Addition of zeros
Add a zero at -3