## Slide 1: Modern Control Systems
Root Locus

## Slide 2: Lecture Outline
Construction of root loci
  Angle and Magnitude Conditions
  Illustrative Examples
Closed loop stability via root locus
Example of Root Locus
  Root Locus of 1st order systems
  Root Locus of 2nd order systems
  Root Locus of Higher order systems

## Slide 3: Construction of Root Loci
Finding the roots of the characteristic equation of degree higher than 3 is laborious and will need computer solution.
A simple method for finding the roots of the characteristic equation has been developed by W. R. Evans and used extensively in control engineering.
This method, called the root-locus method, is one in which the roots of the characteristic equation are plotted for all values of a system parameter.

## Slide 4: Construction of Root Loci
The roots corresponding to a particular value of this parameter can then be located on the resulting graph.
Note that the parameter is usually the gain, but any other variable of the open-loop transfer function may be used.
By using the root-locus method the designer can predict the effects on the location of the closed-loop poles of varying the gain value or adding open-loop poles and/or open-loop zeros.

## Slide 5: Angle & Magnitude Conditions
In constructing the root loci angle and magnitude conditions are important.
Consider the system shown in following figure.
The closed loop transfer function is

## Slide 6: Construction of Root Loci
The characteristic equation is obtained by setting the denominator polynomial equal to zero.
Or
Where G(s)H(s) is a ratio of polynomial in s.
Since G(s)H(s) is a complex quantity it can be split into angle and magnitude part.

## Slide 7: Angle & Magnitude Conditions
The angle of G(s)H(s)=-1 is
Where k=1,2,3…
The magnitude of G(s)H(s)=-1 is

## Slide 8: Angle & Magnitude Conditions
Angle Condition
Magnitude Condition
The values of s that fulfill both the angle and magnitude conditions are the roots of the characteristic equation, or the closed-loop poles.
A locus of the points in the complex plane satisfying the angle condition alone is the root locus.

## Slide 9: Angle and Magnitude Conditions (Graphically)
To apply Angle and magnitude conditions graphically we must first draw the poles and zeros of G(s)H(s) in s-plane.
For example if G(s)H(s) is given by

## Slide 10: Angle and Magnitude Conditions (Graphically)
p
θ1
θ2
ɸ1
θ3
If angle of G(s)H(s) at s=p is equal to ±180o(2k+1) the point p is on root locus.

## Slide 11: Angle and Magnitude Conditions graphically
p
B1
A
B2
B3

## Slide 12: Illustrative Example#1
Apply angle and magnitude conditions (Analytically as well as graphically) on following unity feedback system.

## Slide 13: Illustrative Example#1
Here
For the given system the angle condition becomes

## Slide 14: Illustrative Example#1
For example to check whether s=-0.25 is on the root locus or not we can apply angle condition as follows.

## Slide 15: Illustrative Example#1
Here
And the Magnitude condition becomes

## Slide 16: Illustrative Example#1
Now we know from angle condition that the point s=-0.25 is on the root locus. But we do not know the value of gain K at that specific point.
We can use magnitude condition to determine the value of gain at any point on the root locus.

## Slide 17: Illustrative Example#1

## Slide 18: Illustrative Example#1
Home work:
  check whether s=-0.2+j0.937 is on the root locus or not (Graphically as well as analytically) ?
  check whether s=-1+j2 is on the root locus or not (Graphically as well as analytically) ?

## Slide 19: Illustrative Example#1
Home work:
  If s=-0.2+j0.937 is on the root locus determine the value of gain K at that point.
  If s=-1+j2 is on the root locus determine the value of gain K at that point.

## Slide 20: Construction of root loci
Step-1: The first step in constructing a root-locus plot is to locate the open-loop poles and zeros in s-plane.

## Slide 21: Construction of root loci
Step-2: Determine the root loci on the real axis.
p1
To determine the root loci on real axis we select some test points.
e.g: p1 (on positive real axis).
The angle condition is not satisfied.
Hence, there is no root locus on the positive real axis.

## Slide 22: Construction of root loci
Step-2: Determine the root loci on the real axis.
p2
Next, select a test point on the negative real axis between 0 and –1.
Then
Thus
The angle condition is satisfied. Therefore, the portion of the negative real axis between 0 and –1 forms a portion of the root locus.

## Slide 23: Construction of root loci
Step-2: Determine the root loci on the real axis.
p3
Now, select a test point on the negative real axis between -1 and –2.
Then
Thus
The angle condition is not satisfied. Therefore, the negative real axis between -1 and –2 is not a part of the root locus.

## Slide 24: Construction of root loci
Step-2: Determine the root loci on the real axis.
p4
Similarly, test point on the negative real axis between -3 and – ∞ satisfies the angle condition.
Therefore, the negative real axis between -3 and – ∞ is part of the root locus.

## Slide 25: Construction of root loci
Step-2: Determine the root loci on the real axis.

## Slide 26: Construction of root loci
Step-3: Determine the asymptotes of the root loci.
Asymptote is the straight line approximation of a curve
Actual Curve
Asymptotic Approximation

## Slide 27: Construction of root loci
Step-3: Determine the asymptotes of the root loci.
where
n-----> number of poles
m-----> number of zeros
For this Transfer Function

## Slide 28: Construction of root loci
Step-3: Determine the asymptotes of the root loci.
Since the angle repeats itself as k is varied, the distinct angles for the asymptotes are determined as 60°, –60°, -180°and 180°.
Thus, there are three asymptotes having angles 60°, –60°, 180°.

## Slide 29: Construction of root loci
Step-3: Determine the asymptotes of the root loci.
Before we can draw these asymptotes in the complex plane, we must find the point where they intersect the real axis.
Point of intersection of asymptotes on real axis (or centroid of asymptotes) can be find as out

## Slide 30: Construction of root loci
Step-3: Determine the asymptotes of the root loci.
For

## Slide 31: Construction of root loci
Step-3: Determine the asymptotes of the root loci.

## Slide 32: Home Work
Consider following unity feedback system.
Determine
  Root loci on real axis
  Angle of asymptotes
  Centroid of asymptotes

## Slide 33: Construction of root loci
Step-4: Determine the breakaway point.
  The breakaway point corresponds to a point in the s plane where multiple roots of the characteristic equation occur.
  It is the point from which the root locus branches leaves real axis and enter in complex plane.

## Slide 34: Construction of root loci
Step-4: Determine the break-in point.
  The break-in point corresponds to a point in the s plane where multiple roots of the characteristic equation occur.
  It is the point where the root locus branches arrives at real axis.

## Slide 35: Construction of root loci
Step-4: Determine the breakaway point or break-in point.
The breakaway or break-in points can be determined from the roots of
It should be noted that not all the solutions of dK/ds=0 correspond to actual breakaway points.
If a point at which dK/ds=0 is on a root locus, it is an actual breakaway or break-in point.
Stated differently, if at a point at which dK/ds=0 the value of K takes a real positive value, then that point is an actual breakaway or break-in point.

## Slide 36: Construction of root loci
Step-4: Determine the breakaway point or break-in point.
The characteristic equation of the system is
The breakaway point can now be determined as

## Slide 37: Construction of root loci
Step-4: Determine the breakaway point or break-in point.
Set dK/ds=0 in order to determine breakaway point.

## Slide 38: Construction of root loci
Step-4: Determine the breakaway point or break-in point.
Since the breakaway point must lie on a root locus between 0 and –1, it is clear that s=–0.4226 corresponds to the actual breakaway point.
Point s=–1.5774 is not on the root locus. Hence, this point is not an actual breakaway or break-in point.
In fact, evaluation of the values of K corresponding to s=–0.4226 and s=–1.5774 yields

## Slide 39: Construction of root loci
Step-4: Determine the breakaway point.

## Slide 40: Construction of root loci
Step-4: Determine the breakaway point.

## Slide 41: Home Work
Determine the Breakaway and break in points

## Slide 42: Solution
Differentiating K with respect to s and setting the derivative equal to zero yields;
Hence, solving for s, we find the
break-away and break-in points;
s = -1.45 and 3.82

## Slide 43: Construction of root loci
Step-5: Determine the points where root loci cross the imaginary axis.

## Slide 44: Construction of root loci
Step-5: Determine the points where root loci cross the imaginary axis.
  These points can be found by use of Routh’s stability criterion.
  Since the characteristic equation for the present system is
  The Routh Array Becomes

## Slide 45: Construction of root loci
Step-5: Determine the points where root loci cross the imaginary axis.
The value(s) of K that makes the system marginally stable is 6.
The crossing points on the imaginary axis can then be found by solving the auxiliary equation obtained from the s2 row, that is,
Which yields

## Slide 46: Construction of root loci
Step-5: Determine the points where root loci cross the imaginary axis.
An alternative approach is to let s=jω in the characteristic equation, equate both the real part and the imaginary part to zero, and then solve for ω and K.
For present system the characteristic equation is

## Slide 47: Construction of root loci
Step-5: Determine the points where root loci cross the imaginary axis.
Equating both real and imaginary parts of this equation to zero
Which yields

## Slide 50: Example#1
Consider following unity feedback system.
Determine the value of K such that the damping ratio of a pair of dominant complex-conjugate closed-loop poles is 0.5.

## Slide 51: Example#1
The damping ratio of 0.5 corresponds to

## Slide 52
?

## Slide 53: Example#1
The value of K that yields such poles is found from the magnitude condition

## Slide 55: Example#1
The third closed loop pole at K=1.0383 can be obtained as

## Slide 57: Home Work
Consider following unity feedback system.
Determine the value of K such that the natural undamped frequency of dominant complex-conjugate closed-loop poles is 1 rad/sec.

## Slide 58
-0.2+j0.96

## Slide 59: Example#2
Sketch the root locus of following system and determine the location of dominant closed loop poles to yield maximum overshoot in the step response less than 30%.

## Slide 60: Example#2
Step-1: Pole-Zero Map

## Slide 61: Example#2
Step-2: Root Loci on Real axis

## Slide 62: Example#2
Step-3: Asymptotes

## Slide 63: Example#2
Step-4: breakaway point
-1.55

## Slide 64: Example#2

## Slide 65: Example#2
Mp<30% corresponds to

## Slide 66: Example#2

## Slide 67: Example#2

## Slide 68: Root Locus of 1st Order System
1st order systems (without zero) are represented by following transfer function.
Root locus of such systems is a horizontal line starting from -α and moves towards -∞ as K reaches infinity.
jω
σ
-α
-∞

## Slide 69: Home Work
Draw the Root Locus of the following systems.
1)
2)
3)

## Slide 70: Root Locus of 1st Order System
jω
σ
-α
-β
1st order systems with zero are represented by following transfer function.
Root locus of such systems is a horizontal line starting from -α and moves towards -β as K reaches infinity.

## Slide 71: Home Work
Draw the Root Locus of the following systems.
1)
2)
3)

## Slide 72: Root Locus of 2nd Order System
Second order systems (without zeros) have two poles and the transfer function is given
Root loci of such systems are vertical lines.
jω
σ
-α1
-α2

## Slide 73: Home Work
Draw the Root Locus of the following systems.
1)
2)
3)
4)

## Slide 74: Root Locus of 2nd Order System
Second order systems (with one zero) have two poles and the transfer function is given
Root loci of such systems are either horizontal lines or circular depending upon pole-zero configuration.
jω
σ
-α1
-α2
-β
jω
σ
-α1
-α2
-β
jω
σ
-α1
-α2
-β

## Slide 75: Home Work
Draw the Root Locus of the following systems.
1)
2)
3)

## Slide 76: Example
Sketch the root-locus plot of following system with complex-conjugate open loop poles.

## Slide 77: Example
Step-1: Pole-Zero Mao
Step-2: Determine the root loci on real axis
Step-3: Asymptotes

## Slide 78: Example
Step-4: Determine the angle of departure from the complex-conjugate open-loop poles.
  The presence of a pair of complex-conjugate open-loop poles requires the determination of the angle of departure from these poles.
  Knowledge of this angle is important, since the root locus near a complex pole yields information as to whether the locus originating from the complex pole migrates toward the real axis or extends toward the asymptote.

## Slide 79: Example
Step-4: Determine the angle of departure from the complex-conjugate open-loop poles.

## Slide 80: Example
Step-5: Break-in point

## Slide 82: Root Locus of Higher Order System
Third order System without zero

## Slide 83: Root Locus of Higher Order System
Sketch the Root Loci of following unity feedback system

## Slide 84
Let us begin by calculating the asymptotes. The real-axis intercept is evaluated as;
The angles of the lines that intersect at - 4/3, given by

## Slide 85
The Figure shows the complete root locus as well as the asymptotes that were just calculated.

## Slide 86
Example: Sketch the root locus for the system with the characteristic equation of;
Number of finite poles = n = 4.
Number of finite zeros = m = 1.
Number of asymptotes = n - m = 3.
Number of branches or loci equals to the number of finite poles (n) = 4.
The portion of the real-axis between, 0 and -2, and between, -4 and -∞, lie on the root locus for K > 0.
Using Eq. (v), the real-axis asymptotes intercept is evaluated as;
The angles of the asymptotes that intersect at - 3, given by Eq. (vi), are;
For K = 0, θa = 60o
For K = 1, θa = 180o
For K = 2, θa = 300o

## Slide 87
The root-locus plot of the system is shown in the figure below.
It is noted that there are three asymptotes. Since n – m = 3.
The root loci must begin at the poles; two loci (or branches) must leave the double pole at s = -4.
Using Eq. (vii), the breakaway point, σ, can be determine as;
The solution of the above equation is

## Slide 88: Example: Sketch the root loci for the system.
A root locus exists on the real axis between points s = –1 and s = –3.6.
The intersection of the asymptotes and the real axis is determined as,
The angles of the asymptotes that intersect at – 1.3, given by Eq. (vi), are;
Since the characteristic equation is
We have
For K = 0, θa = 90o
For K = 1, θa = -90o or 270o
(a)

## Slide 89
The breakaway and break-in points are found from Eq. (a) as,
From which we get,
Point s = 0 corresponds to the actual breakaway point. But points are neither breakaway nor break-in points, because the corresponding gain values K become complex quantities.

## Slide 90
To check the points where root-locus branches may cross the imaginary axis, substitute into the characteristic equation, yielding.
Notice that this equation can be satisfied only if
Because of the presence of a double pole at the origin, the root locus is tangent to the axis at .
The root-locus branches do not cross the axis.
The root loci of this system is shown in the Figure.