## Slide 1: Modern Control Systems
Introduction to State Space Modeling & Analysis

## Slide 2: Lecture Outline
Introduction to state space
  Basic Definitions
  State Equations
  State Diagram
  State Controllability
  State Observability
  Output Controllability

## Slide 3: Introduction
Modern control theory is contrasted with conventional control theory in that the former is applicable to multiple-input, multiple-output systems, which may be linear or nonlinear, time invariant or time varying, while the latter is applicable only to linear time invariant single-input, single-output systems.

## Slide 4: Definitions
State of a system: We define the state of a system at time t0 as the amount of information that must be provided at time t0, which, together with the input signal u(t) for t  t0, uniquely determine the output of the system for all t  t0.
State Variable: The state variables of a dynamic system are the smallest set of variables that determine the state of the dynamic system.
State Vector: If n variables are needed to completely describe the behaviour of the dynamic system then n variables can be considered as n components of a vector x, such a vector is called state vector.
State Space: The state space is defined as the n-dimensional space in which the components of the state vector represents its coordinate axes.

## Slide 5: Definitions
Let x1 and x2 are two states variables that define the state of the system completely .
Two Dimensional State space
State (t=t1)
State
Vector
State space of a Vehicle
Velocity
Position
State (t=t1)

## Slide 6: State Space Equations
In state-space analysis we are concerned with three types of variables that are involved in the modeling of dynamic systems: input variables, output variables, and state variables.
The dynamic system must involve elements that memorize the values of the input for t> t1 .
Since integrators in a continuous-time control system serve as memory devices, the outputs of such integrators can be considered as the variables that define the internal state of the dynamic system.
Thus the outputs of integrators serve as state variables.
The number of state variables to completely define the dynamics of the system is equal to the number of integrators involved in the system.

## Slide 7: State Space Equations
Assume that a multiple-input, multiple-output system involves integrators.
Assume also that there are inputs and outputs .
Define outputs of the integrators as state variables: .
Then the system may be described by

## Slide 8: State Space Equations
The outputs of the system may be given as.
If we define

## Slide 9: State Space Modelling
State space equations can then be written as
If vector functions f and/or g involve time t explicitly, then the system is called a time varying system.
State Equation
Output Equation

## Slide 10: State Space Modelling
If above equations are linearised about the operating state, then we have the following linearised state equation and output equation:

## Slide 11: State Space Modelling
If vector functions f and g do not involve time t explicitly then the system is called a time-invariant system.
In this case, state and output equations can be simplified to

## Slide 12: Example-1
Consider the mechanical system shown in figure. We assume that the system is linear. The external force u(t) is the input to the system, and the displacement y(t) of the mass is the output. The displacement y(t) is measured from the equilibrium position in the absence of the external force. This system is a single-input, single-output system.
From the diagram, the system equation is
This system is of second order. This means that the system involves two integrators. Let us define state variables and as

## Slide 13: Example-1
Then we obtain
Or
The output equation is

## Slide 14: Example-1
In a vector-matrix form,

## Slide 15: Example-1
State diagram of the system is
1/s
1/s
-k/m
-b/m
1/m

## Slide 16: Example-1
State diagram in signal flow and block diagram format
1/s
1/s
-k/m
-b/m
1/m

## Slide 17: Example-2
State space representation of armature Controlled D.C Motor.
ea is armature voltage (i.e. input) and  is output.
ea
ia
T
Ra
La
J

B
eb
Vf=constant


## Slide 18
Example-2
Choosing as state variables
Since is output of the system therefore output equation is given as

## Slide 19: State Controllability
A system is completely controllable if there exists an unconstrained control u(t) that can transfer any initial state x(to) to any other desired location x(t) in a finite time, to ≤ t ≤ T.
controllable
uncontrollable

## Slide 20: State Controllability
Controllability Matrix CM
System is said to be state controllable if

## Slide 21: State Controllability (Example)
Consider the system given below
State diagram of the system is

## Slide 22: State Controllability (Example)
Controllability matrix CM is obtained as
Thus
Since therefore system is not completely state controllable.

## Slide 23: State Observability
A system is completely observable if and only if there exists a finite time T such that the initial state x(0) can be determined from the observation history y(t) given the control u(t), 0≤ t ≤ T.
observable
unobservable

## Slide 24: State Observability
Observable Matrix (OM)
The system is said to be completely state observable if

## Slide 25: State Observability (Example)
Consider the system given below
OM is obtained as
Where

## Slide 26: State Observability (Example)
Therefore OM is given as
Since therefore system is not completely state observable.

## Slide 28: Output Controllability
Output controllability describes the ability of an external input to move the output from any initial condition to any final condition in a finite time interval.
Output controllability matrix (OCM) is given as

## Slide 29: Home Work
Check the state controllability, state observability and output controllability of the following system